## Slide 1
MSc SEMINAR
University of Babylon
Parallel image compression using high-performance computing strategies
LBG vector quantization · delta coding · Huffman · speed-aware MPI on a hybrid P/E-core CPU
Presented by MSc. Student Ibtihal Hussien
Supervised by Dr. Ahmed Badri · Dr. Esraa Hadi
Notes: Introduce the topic: a parallel (MPI) LBG vector-quantization image compressor, evaluated on a hybrid CPU with 6 performance and 8 efficiency cores.

## Slide 2: Outline
AGENDA
1
Introduction
2
Related work
3
Research problems
4
Research objective
5
Proposed method
6
Proposed parallel computing strategies
7
Results and discussion
8
Conclusion
9
References
Notes: Nine parts, following the structure of the seminar: introduction, related work, problems, objectives, the proposed method, the parallel strategy, results, conclusion and references.

## Slide 3: Why compress images, and how?
1 · INTRODUCTION
Storage
Large image collections need less space.
Transmission
Smaller files reach the receiver sooner.
Computation
Compression itself must be fast enough to use.
Lossless
Perfect reconstruction. Used for documents and archives: RLE, Huffman, LZW, BWT.
Lossy (this work)
Some data is discarded for a much smaller file: VQ, DCT, DWT, DPCM. Here: vector quantization + delta + Huffman.
Notes: Compression reduces storage and bandwidth. VQ is lossy; in this work the compressed size includes the codebook and the Huffman table, so the reported ratio is the real ratio.

## Slide 4: Why parallelize LBG codebook training?
1 · INTRODUCTION
16,384
training vectors per 512×512 image (4×4 blocks)
64
codewords, 16 dimensions each
≈ 150
Lloyd iterations (132–186 per gray image)
1.05 M
distance evaluations per iteration at K = 64
The assignment step is data-parallel
Each training vector is assigned independently; only the per-cluster sums and counts must be combined (one MPI_Allreduce per iteration).
Sequential LBG ≈ 77% (gray) and 81% (color) of the total time
So accelerating LBG is the highest-value target, and the remaining stages (I/O, delta, Huffman, reconstruction) set the limit on total speedup.
Notes: LBG is iterative: every iteration compares every training vector with every codeword. This is the dominant cost of the sequential compressor (about 77% of the total time for grayscale images).

## Slide 5: Evaluation metrics
1 · INTRODUCTION
Compression ratio
CR = original bytes / (codebook + Huffman table + Huffman data)
PSNR
10·log10(255² / MSE), in dB
SSIM
11×11 Gaussian window, σ = 1.5; color = mean of 3 channels
Speedup S
S = T_seq / T_P
Efficiency E
E = S / P
Karp–Flatt e
e = (1/S − 1/P) / (1 − 1/P): serial fraction
Throughput Θ
Θ = N · I / T_LBG (vector-iterations per second)
Notes: System CR includes the codebook (1,024 bytes) and the Huffman table, so it is the true compression ratio. PSNR and SSIM measure fidelity. Speedup, efficiency, Karp–Flatt and throughput measure the parallel performance.

## Slide 6: Related work: image-compression studies
2 · RELATED WORK
Study | Method | Reported result | Observation
Thomas et al., 2025 | Integer DWT + reduction + Huffman | Lena: CR 1.52, PSNR 54.28 dB, SSIM 0.9985 | Near-lossless; low CR; sequential
Ranjan & Kumar, 2023 | 2D DWT + PCA + canonical Huffman | Lena 512: CR 4.41, PSNR 34.78 dB | Moderate CR; no parallelism
Bilal et al., 2024 | Fast LBG (FLBG), rescaling | 50.2% less complexity, 20% less memory | Algorithmic speedup; sequential
Paul et al., 2024 | K-means + DWT (K-DWT) | Kodak: CR 15.39, PSNR 30.51 dB, SSIM 0.8978 | No timing values reported
Takeaway: published compression studies are sequential and span very different rate–distortion regimes (CR from 1.4 to 15).
Notes: These studies work at very different operating points: from near-lossless (CR about 1.5) to high compression. Values are taken from the papers' tables.

## Slide 7: Related work: parallel studies
2 · RELATED WORK
Study | Application | Resources | Speedup (baseline)
Tanović et al., 2024 | Parallel k-means, image classification | 12 cores, OpenMP + MPI | up to 10.2× (not stated in abstract)
Papakyriakou et al., 2025 | MPI k-means, 75 M synthetic points | 2–48 MPI processes, Raspberry Pi | ≈10.05× (vs 2 processes)
Bystrov et al., 2023 | Discrete-element simulation | 8 heterogeneous containers | up to 6.0× (vs sequential)
Zangana, 2025 | Hybrid image compression (bitplane + DWT + predictive) | 1–16 GPUs, CUDA / OpenCL | 9.09× at 16 GPUs (vs 1 GPU)
Takeaway: reported speedups are 6–10×, but none parallelizes LBG codebook training for image compression with speed-aware distribution.
Notes: Speedups come from different applications and baselines, so they are context, not a ranking. Papakyriakou uses the two-process run as baseline. Zangana's 9.09x is derived from the 1-GPU and 16-GPU times.

## Slide 8: Research problems
3 · RESEARCH PROBLEMS
1 Delay in sending data
Large images take a long time to transmit over a network.
2 Big data storage
Image collections need a large amount of storage.
3 Complexity versus time
A good compression ratio needs complex methods (here: iterative LBG training), so execution time becomes high.
4 Acceptable quality
The reconstructed image must remain of acceptable quality (PSNR, SSIM).
Notes: Four problems motivate the work: delay in sending data, big data storage, the cost of obtaining a good compression ratio, and the need for acceptable quality.

## Slide 9: Research objective
4 · RESEARCH OBJECTIVE
1
Objective
Develop an image-compression method with a good compression ratio, using parallel processing to reduce its execution time.
How this work meets it
LBG vector quantization + delta + Huffman coding, parallelized with MPI (Equal and speed-aware Adaptive distribution).
2
Objective
Maintain the quality of the reconstructed image as much as possible.
How this work meets it
Quality measured by PSNR and SSIM; the parallel result is verified to be identical to the sequential one (MD5).
Notes: Two objectives: a good compression ratio with parallel speed, and preserved quality. The right-hand column shows how the work meets each one.

## Slide 10: What this work contributes
4 · RESEARCH OBJECTIVE
Compression pipeline
4×4 blocks → LBG (K = 64) → delta → Huffman; system CR counts every byte.
MPI parallel LBG
Scatterv + Allreduce SPMD design, exact and independent of process count.
Speed-aware distribution
Adaptive vector allocation for P-cores and E-cores; 17–28% faster LBG than Equal at P = 8–14.
Rigorous evaluation
Median of 5, CPU binding, Karp–Flatt, throughput, and MD5-verified equivalence.
Notes: Four contributions: the pipeline, the parallel implementation, the Adaptive distribution for hybrid CPUs, and the measurement and verification methodology.

## Slide 11: Compression pipeline
5 · PROPOSED METHOD
Image
512×512
8-bit
4×4 blocks
16,384 vectors
16-D
LBG-VQ
codebook K = 64
Index map
one label
per block
Delta coding
offset 128
Huffman
entropy code
Bitstream
data + table
+ codebook
Encoder
The expensive step is LBG training: that is the stage parallelized with MPI. Delta and Huffman run on rank 0.
Decoder
Huffman decode → undo delta → look up each index in the codebook → rebuild the 4×4 blocks.
Notes: The image is split into 4x4 blocks, each block is a 16-dimensional vector. LBG builds a 64-vector codebook. Each block is replaced by an index, the index sequence is delta-coded and Huffman-coded.

## Slide 12: From pixels to 16-dimensional vectors
5 · PROPOSED METHOD
96×96 region of Cameraman, with the 4×4 block grid
One block = one vector
x = (p₁, p₂, …, p₁₆) with 16 pixel values 0…255
A 512×512 image gives 16,384 training vectors.
Vector quantization
Each vector is replaced by the index of its nearest codeword. With K = 64 the codebook costs only 64 × 16 = 1,024 bytes, and each index needs at most 6 bits before entropy coding.
Notes: Zoom on a Cameraman region: the image is a grid of 4x4 blocks; each block becomes one vector and later one codeword index.

## Slide 13: LBG: splitting + Lloyd iterations
5 · PROPOSED METHOD
K = 1
K = 2
K = 4
K = 8
K = 16
K = 32
K = 64
split ×2 → Lloyd until convergence → split again
1 Split
Each codeword c → c(1+δ) and c(1−δ), δ = 0.01
2 Assign
Every vector goes to its nearest codeword (squared Euclidean distance)
3 Update
Each codeword becomes the mean of its assigned vectors
4 Test
Stop when |ΔD| / D ≤ ε = 10⁻⁴ or after 100 iterations
Typical run: about 150 Lloyd iterations in total over the six stages.
Notes: Start from the global mean; split every codeword by a factor (1 plus or minus delta), then run Lloyd iterations until the relative distortion change is below epsilon. Repeat until K = 64.

## Slide 14: Delta coding lowers the entropy of the indices
5 · PROPOSED METHOD
Chart: bits per index
| Lena | Boat | Cameraman | Peppers
Entropy of indices | 5.393 | 5.237 | 5.165 | 5.396
Entropy after delta | 4.665 | 4.061 | 3.682 | 4.365
5.30 → 4.19
mean entropy in bits per index (grayscale), a 1.1-bit reduction.
4.23 bits/index
Huffman rate, only 0.039 bit above the entropy: 29.5% less than fixed 6-bit indices.
Notes: LBG orders codewords so that neighbouring blocks tend to have close indices; coding the difference between consecutive indices lowers the entropy. Huffman coding then reaches within about 0.04 bit of the entropy.

## Slide 15: System compression ratio: every byte counted
5 · PROPOSED METHOD
Chart: Mean over the four grayscale images
| Fixed 8-bit indices | Fixed 6-bit indices | Delta + Huffman
System CR | 15.06 | 19.69 | 25.92
+31.6%
gain of delta + Huffman over 6-bit indices
Compressed size counts:
codebook: 64 × 16 = 1,024 bytes
Huffman table: 4 bytes per used symbol
Huffman-coded index data
CR is computed from these sizes; the program does not write a stored file. A 5-byte table entry would lower CR by about 1%.
Notes: The system CR divides the original bytes by codebook (1,024 bytes) + Huffman table + Huffman data. Delta + Huffman raises the ratio from 15.06 (8-bit indices) to 25.92 on average.

## Slide 16: Test images
5 · PROPOSED METHOD
Lena
Cameraman
Peppers
F-16
Gold Hill
Grayscale (4)
Lena, Boat, Cameraman, Peppers: 1 byte per pixel, 16,384 vectors.
Color (4)
Lena, Peppers, F-16, Gold Hill: R, G, B coded as three independent channels, CR and MSE pooled.
Notes: Eight 512x512 images: four grayscale (Lena, Boat, Cameraman, Peppers) and four color (Lena, Peppers, F-16, Gold Hill). Color images are processed per R, G, B channel. Thumbnails shown here are the images available for this deck.

## Slide 17: MPI design: SPMD with one Allreduce per iteration
6 · PROPOSED PARALLEL COMPUTING STRATEGIES
Rank 0
read image,
build vectors
Bcast + Scatterv
parameters,
vector blocks
Local assign
nearest codeword,
partial sums
Allreduce
sums + counts
(double)
Update
new codebook
on every rank
Gatherv
labels to rank 0
loop: repeat until converged
Why the result does not depend on P
Training vectors are integers 0…255, so sums and counts are exact in double precision and independent of summation order. The iteration count was the same for every P.
What stays on rank 0
Image I/O, delta coding, Huffman, reconstruction and metrics. These stages limit the total speedup (Amdahl).
Notes: Rank 0 reads the image and builds the vectors, then broadcasts parameters and scatters the vectors. Every iteration: assign locally, Allreduce the partial sums and counts, update the codebook. Finally the labels are gathered on rank 0 for delta and Huffman coding.

## Slide 18: Equal vs Adaptive workload distribution
6 · PROPOSED PARALLEL COMPUTING STRATEGIES
Equal
P-core rank
P-core rank
E-core rank
E-core rank
Adaptive (speed-weighted)
P-core rank
P-core rank
E-core rank
E-core rank
schematic: share of training vectors per rank
Equal (default for P ≤ 4)
Each rank gets N/P vectors. Simple, but the slowest rank sets the pace.
Adaptive (default for P > 4)
calibrate_speed() times a short kernel on each rank; shares are proportional to measured speed.
Notes: On a hybrid CPU, equal shares make P-cores wait for the slower E-cores at every Allreduce. Adaptive measures each rank's speed with a micro-benchmark and gives faster ranks more vectors, so all ranks finish together.

## Slide 19: Platform and measurement protocol
6 · PROPOSED PARALLEL COMPUTING STRATEGIES
6 P + 8 E
Intel Core i7-13650HX: 14 cores, hybrid
P = 2 … 14
MPI processes, Open MPI, one per core
Median of 5
runs per configuration and image
CPU governor: performance, AC power
mpirun --bind-to core: one rank per core
Sequential program pinned to CPU 6
gcc / mpicc -O2; LBG time excludes calibration, Total includes it
Notes: All timings are medians of five runs under identical conditions. The sequential reference program is pinned to one core, so speedup is relative to a separate sequential implementation.

## Slide 20: Verification: parallel = sequential
6 · PROPOSED PARALLEL COMPUTING STRATEGIES
Run | Processes | Strategy
1 Sequential reference | 1 | –
2 Parallel | 4 | Equal (default)
3 Parallel | 14 | Adaptive (default)
4 Parallel | 14 | Equal (forced)
8 / 8
images with identical metrics and identical MD5
same iterations
LBG iteration count constant for every P
Scope of the claim
Compared: CR, MSE, PSNR, SSIM, iterations and the MD5 of the reconstructed BMP (external md5sum tool). The codebooks and bitstreams were not compared directly, so equivalence is stated for the tested configurations.
Notes: For every image the sequential program and three parallel runs (P=4, P=14 Adaptive, P=14 Equal) give identical CR, MSE, PSNR, SSIM and iteration count, and the md5sum of the reconstructed BMP files is identical. md5sum is an external tool, not part of the algorithm. The check covers the reconstructed image and metrics, not the codebook or bitstream directly.

## Slide 21: Parameter study: block size and codebook size
7 · RESULTS AND DISCUSSION
Chart: System compression ratio
| 2x2 K64 | 4x4 K128 | 4x4 K64 | 4x4 K32 | 8x8 K64
CR | 7.578 | 19.39 | 25.918 | 34.62 | 37.88
Chart: PSNR (dB)
| 2x2 K64 | 4x4 K128 | 4x4 K64 | 4x4 K32 | 8x8 K64
PSNR | 33.825 | 30.675 | 29.485 | 28.273 | 26.322
4×4 / K = 64: CR 25.9, PSNR 29.5 dB. The trade-off is monotonic: more compression, less fidelity.
Notes: Mean over the four grayscale images. Larger blocks and smaller codebooks give higher compression and lower quality. 4x4 with K=64 is the chosen balance.

## Slide 22: Grayscale results (4×4 blocks, K = 64)
7 · RESULTS AND DISCUSSION
Chart: CR
| Lena | Boat | Cameraman | Peppers
CR | 23.5 | 26.54 | 28.88 | 24.75
Chart: PSNR (dB)
| Lena | Boat | Cameraman | Peppers
PSNR | 29.67 | 29.11 | 29.75 | 29.41
Chart: SSIM
| Lena | Boat | Cameraman | Peppers
SSIM | 0.819 | 0.8394 | 0.8855 | 0.7624
25.92
mean system CR
29.49 dB
mean PSNR
0.8266
mean SSIM
Notes: Per-image system CR and PSNR for the four grayscale images; mean CR 25.92, PSNR 29.49 dB, SSIM 0.8266.

## Slide 23: Color results (R, G, B coded independently)
7 · RESULTS AND DISCUSSION
Chart: CR
| Lena | Peppers | F-16 | Gold Hill
CR | 24 | 23.89 | 26.44 | 23.54
Chart: PSNR (dB)
| Lena | Peppers | F-16 | Gold Hill
PSNR | 28.91 | 28.35 | 29.47 | 28.45
Chart: SSIM
| Lena | Peppers | F-16 | Gold Hill
SSIM | 0.7594 | 0.6964 | 0.8539 | 0.752
24.47
mean system CR
28.80 dB
mean PSNR
0.7654
mean SSIM
Notes: Per-image values for the four color images; mean CR 24.47, PSNR 28.80 dB, SSIM 0.7654. CR and MSE are pooled over the three channels; SSIM is the mean of the three channel SSIMs.

## Slide 24: Visual result: Cameraman
7 · RESULTS AND DISCUSSION
Original
Reconstructed (K = 64)
original
reconstructed
4× zoom of the same 96×96 region
28.88
CR
29.75
PSNR dB
SSIM 0.8855 · MSE 68.84
At CR ≈ 29 the image remains recognisable; fine textures show the 4×4 block structure of VQ.
Notes: Reconstruction by the sequential program: CR 28.88, MSE 68.84, PSNR 29.75 dB, SSIM 0.8855. The block structure of VQ is visible in the 4x zoom.

## Slide 25: Quality at matched compression ratio
7 · RESULTS AND DISCUSSION
Chart: PSNR at approximately matched CR
| Lena | Boat | Cameraman | Peppers
Proposed VQ | 29.67 | 29.11 | 29.75 | 29.41
DWT + Huffman | 26.83 | 26.05 | 26.56 | 26.53
JPEG | 33.14 | 31.37 | 34.01 | 32.24
JPEG 2000 | 35.48 | 33.64 | 37.17 | 33.42
How to read it
Each image: CR matched within ≈ 2%.
JPEG 2000 > JPEG > proposed VQ > generic DWT+Huffman in PSNR.
VQ gives a simple, parallelizable codec with a fast decoder.
Notes: At approximately the same CR, JPEG 2000 and JPEG reach higher PSNR than the proposed VQ codec, while the generic DWT+Huffman baseline developed in this work is lower. The proposed codec is not a quality leader; its contribution is the parallel framework. The DWT baseline is a generic, controlled implementation, not a published method.

## Slide 26: Where the sequential time goes
7 · RESULTS AND DISCUSSION
Chart: Grayscale (sequential)
| LBG training | Other stages
Grayscale (sequential) | 0.2557 | 0.0761
Chart: Color (sequential)
| LBG training | Other stages
Color (sequential) | 0.7827 | 0.1817
77%
gray
81%
color
Mean sequential times: gray LBG 0.256 s of 0.332 s total; color LBG 0.783 s of 0.964 s.
Notes: In the sequential program LBG is 77% of the total time for grayscale and 81% for color. The remaining stages (I/O, delta, Huffman, reconstruction, metrics) are the part that does not scale.

## Slide 27: LBG speedup versus number of processes
7 · RESULTS AND DISCUSSION
Chart: MPI processes P
| 1 | 2 | 4 | 6 | 8 | 10 | 12 | 14
Ideal (S = P) | 1 | 2 | 4 | 6 | 8 | 10 | 12 | 14
Measured (mean of 8 images) | 1 | 1.9362 | 3.7925 | 5.4112 | 6.3025 | 7.3575 | 8.2275 | 9.1937
9.19×
LBG speedup at P = 14 (range 9.10–9.24)
65.7%
parallel efficiency at P = 14
Efficiency is high through the 6 P-cores, then limited by slower E-cores.
Notes: Mean over the eight images. 9.19x at P=14, 65.7% efficiency. Speedup is almost linear up to P=6 (the P-cores) and then grows more slowly because E-cores are slower.

## Slide 28: Efficiency and the Karp–Flatt metric
7 · RESULTS AND DISCUSSION
Chart: LBG parallel efficiency (%)
| 2 | 4 | 6 | 8 | 10 | 12 | 14
Efficiency | 96.8 | 94.8 | 90.2 | 78.8 | 73.6 | 68.6 | 65.7
Chart: Karp–Flatt serial fraction (LBG)
| 2 | 4 | 6 | 8 | 10 | 12 | 14
Karp–Flatt (LBG) | 0.033 | 0.018 | 0.022 | 0.038 | 0.04 | 0.042 | 0.04
LBG serial fraction ≈ 0.04 for P ≥ 8: the loss is the E-core speed gap, not communication.
Notes: Efficiency = S/P. It falls after P=6 where E-cores join. The Karp-Flatt serial fraction of the LBG stage stays about 0.04 for P>=8, so there is no growing parallel overhead; the Total stage has about 0.14 (gray) and 0.08 (color) because of the non-parallel stages.

## Slide 29: Throughput of the LBG stage
7 · RESULTS AND DISCUSSION
Chart: MPI processes P (1 = sequential)
| 1 | 2 | 4 | 6 | 8 | 10 | 12 | 14
Grayscale | 9.7 | 18.7 | 36.6 | 52.2 | 60.6 | 71 | 79.3 | 88.7
Color (per channel) | 9.8 | 19 | 37.3 | 53.2 | 62 | 72.3 | 80.8 | 90.3
9.7 → 88.7
M vec-it/s, gray (P = 1 → 14)
9.8 → 90.3
M vec-it/s, color per channel
Throughput scales with P for both modes, as expected for a data-parallel kernel.
Notes: Throughput = N*I/T_LBG in millions of vector-iterations per second (per channel for color). It grows from about 9.7-9.8 M/s sequentially to about 89-90 M/s at P=14, an increase of 9.2x.

## Slide 30: Total speedup: Amdahl in action
7 · RESULTS AND DISCUSSION
Chart: MPI processes P
| 1 | 2 | 4 | 6 | 8 | 10 | 12 | 14
LBG stage (mean) | 1 | 1.9362 | 3.7925 | 5.4112 | 6.3025 | 7.3575 | 8.2275 | 9.1937
Total, color | 1 | 1.865 | 3.45 | 4.6525 | 5.0425 | 5.7225 | 6.2925 | 6.8425
Total, grayscale | 1 | 1.7675 | 2.9925 | 3.79 | 4.005 | 4.39 | 4.72 | 5.0025
5.00×
total speedup, gray (P = 14)
6.84×
total speedup, color (P = 14)
Karp–Flatt of Total ≈ 0.14 (gray) and 0.08 (color): the non-parallel stages.
Notes: Total speedup includes I/O, delta, Huffman, reconstruction and metrics, which stay on rank 0. At P=14 the total speedup is 5.00x for grayscale and 6.84x for color, much lower than the 9.19x of the LBG stage.

## Slide 31: Time breakdown: sequential vs P = 14
7 · RESULTS AND DISCUSSION
Chart: Grayscale: mean time (s)
| P = 1 | P = 14
LBG training | 0.2557 | 0.0279
Other stages | 0.0761 | 0.0384
Chart: Color: mean time (s)
| P = 1 | P = 14
LBG training | 0.7827 | 0.085
Other stages | 0.1817 | 0.0561
Share of non-LBG stages in the total: 23% → 58% (gray) and 19% → 40% (color).
Notes: Mean stage times in seconds. At P=14 the LBG stage shrinks by 9.2x, but the other stages shrink only 2.0x (gray) and 3.2x (color), so their share of the total grows from 23% to 58% (gray) and from 19% to 40% (color).

## Slide 32: Equal vs Adaptive: LBG execution time
7 · RESULTS AND DISCUSSION
Chart: Grayscale: mean LBG time (s)
| 2 | 4 | 6 | 8 | 10 | 12 | 14
Equal | 0.1321 | 0.0675 | 0.0473 | 0.0565 | 0.0456 | 0.0389 | 0.0337
Adaptive | 0.1322 | 0.0675 | 0.0474 | 0.0406 | 0.0349 | 0.0313 | 0.0279
Chart: Color: mean LBG time (s)
| 2 | 4 | 6 | 8 | 10 | 12 | 14
Equal | 0.4042 | 0.2053 | 0.1442 | 0.1727 | 0.1391 | 0.1186 | 0.1025
Adaptive | 0.4044 | 0.2061 | 0.1442 | 0.1236 | 0.1062 | 0.0949 | 0.0849
Equal and Adaptive coincide for P ≤ 6; for P ≥ 8 Adaptive is faster on all 8 images.
Notes: Mean LBG time in seconds. For P up to 6 the two strategies are equivalent (all ranks on P-cores). From P=8, when E-cores are used, Adaptive is clearly faster.

## Slide 33: Adaptive gain over Equal distribution
7 · RESULTS AND DISCUSSION
Chart: MPI processes P
| 2 | 4 | 6 | 8 | 10 | 12 | 14
LBG time reduction (%) | -0.1 | -0.2 | -0.1 | 28.3 | 23.6 | 19.8 | 17.2
Total time reduction (%) | -0.3 | -0.6 | -0.6 | 17.9 | 13.7 | 10.7 | 8.8
28.3%
LBG time saved at P = 8
17.2%
LBG time saved at P = 14
No difference for P ≤ 6 (±1%): only P-cores are used.
Notes: Reduction of execution time with Adaptive relative to Equal, mean over the eight images (mean of per-image reductions). LBG: 28.3, 23.6, 19.8, 17.2 percent at P=8, 10, 12, 14. Total: 17.9, 13.7, 10.7, 8.8 percent.

## Slide 34: Comparison with reported studies: compression
7 · RESULTS AND DISCUSSION
Image | Reference | CR | PSNR (dB) | Time ratio
Lena | Thomas et al. [6] | 1.52 | 54.28 | –
 | Ranjan & Kumar [16] | 4.41 | 34.78 | –
 | This work | 23.50 | 29.67 | 9.21×
Boat | Thomas et al. [6] | 1.41 | 54.07 | –
 | This work | 26.54 | 29.11 | 9.22×
Cameraman | Bilal et al. [17] | – | 25.3–26.8* | 2.61×
 | This work | 28.88 | 29.75 | 9.10×
* at ≤ 0.625 bpp. “–” = not reported. Time ratio is computed within each study (LBG/FLBG time vs sequential/MPI time at P = 14); the mechanisms and hardware differ. Indicative only: images, implementations and size accounting differ.
Different operating points: near-lossless wavelet methods vs a high-compression VQ codec (CR 23–29).
Notes: A contextual comparison only. The studies operate at different compression ratios and use different images and size accounting; values are indicative. The time ratio is computed within each study: LBG/FLBG time in Bilal et al.; sequential/MPI LBG time at P=14 in this work.

## Slide 35: Comparison with reported studies: parallel speedup
7 · RESULTS AND DISCUSSION
Study | Application | Resources | Baseline | Speedup
Tanović 2024 | k-means, image classification | 12 cores | not stated | up to 10.2×
Papakyriakou 2025 | k-means, 75 M points | 2–48 MPI processes | 2 processes | ≈10.05×
Bystrov 2023 | DEM simulation | 8 heterogeneous containers | sequential | up to 6.0×
This work | LBG image compression | 14 MPI processes (6 P + 8 E) | sequential | 9.19× LBG; 5.00× / 6.84× total
Papakyriakou: 181.83 s → 18.09 s, efficiency 41.89% at 48 processes, relative to the two-process baseline. The studies differ in application, workload, hardware, process count and speedup baseline: contextual comparison, not a ranking.
The speedup is of the same order as the reported 6–10×. The contribution is the speed-aware distribution on a hybrid CPU (17–28% faster LBG than Equal), not a higher absolute speedup.
Notes: Contextual comparison. This work reports speedup against a separate sequential program. The 9.19x is the mean LBG-stage speedup over the eight images; the total speedup includes the non-parallel stages. The reported speedups are of the same order but are not a ranking.

## Slide 36: Limitations
8 · CONCLUSION
One platform
A single hybrid CPU (i7-13650HX); results may differ on other CPUs.
Small problem size
512×512 images limit scalability at high P (≈ 1.5–2 ms per sequential iteration).
Non-parallel stages
I/O, delta, Huffman and reconstruction stay on rank 0: 58% of total time at P = 14 (gray).
Quality vs standards
At matched CR, JPEG and JPEG 2000 reach higher PSNR than VQ with K = 64.
Notes: Be explicit about the limits: one CPU platform, a modest problem size, a non-parallel part, and quality below standard codecs at the same CR.

## Slide 37: Conclusion
8 · CONCLUSION
25.92
mean CR (gray), PSNR 29.5 dB
9.19×
LBG speedup at P = 14
5.0 / 6.8×
total speedup gray / color
17–28%
less LBG time with Adaptive (P = 8–14)
A parallel LBG vector-quantization compressor (4×4 blocks, K = 64, delta + Huffman) reaches CR ≈ 24–26 at PSNR ≈ 29 dB.
MPI parallelization preserves the results in all tested configurations and cuts LBG time 9.2× on 14 processes (65.7% efficiency).
Speed-aware (Adaptive) distribution reduces LBG time by 17–28% against Equal on the hybrid P/E-core CPU.
Total speedup (5.0× / 6.8×) is bounded by the non-parallel stages, as the Karp–Flatt analysis shows.
Notes: Summarize: the compressor, the exact parallelization, the speedup, the Adaptive gain, and the quality.

## Slide 38: Future work
8 · CONCLUSION
Parallelize the remaining stages
Delta, Huffman and reconstruction are 58% of total time at P = 14.
Hybrid MPI + OpenMP
Combine process- and thread-level parallelism on the hybrid CPU.
GPU acceleration
Offload the assignment step, the dominant kernel.
Better entropy coding
Canonical Huffman and a 5-byte-per-symbol table accounting; larger images.
Notes: Natural extensions: parallelize the remaining stages, hybrid MPI+OpenMP, GPU, and entropy coding improvements.

## Slide 39: References
9 · REFERENCES
[1] H. M. Zangana (2025). Design and implementation of a novel parallel algorithm for efficient image compression in high-performance computing. EAI Endorsed Trans. AI and Robotics, 4.
[2] S. Thomas, A. Krishna, S. Govind, A. K. Sahu (2025). A novel image compression method using wavelet coefficients and Huffman coding. J. Eng. Res., 13, 361–370.
[3] R. Ranjan, P. Kumar (2023). An improved image compression algorithm using 2D DWT and PCA with canonical Huffman encoding. Entropy, 25, 1382.
[4] M. Bilal, Z. Ullah, O. Mujahid, T. Fouzder (2024). Fast Linde–Buzo–Gray (FLBG) algorithm for image compression through rescaling using bilinear interpolation. J. Imaging, 10, 124.
[5] R. K. Paul et al. (2024). Image compression scheme based on optimized K-means clustering and higher-level decomposed DWT. Procedia Comput. Sci., 235, 642–655.
[6] A. Tanović et al. (2024). Implementation of parallel K-means algorithm for image classification using OpenMP and MPI libraries. ZINC 2024.
[7] D. Papakyriakou, I. S. Barbounakis (2025). Parallel k-means benchmarking on a CPU-bound Beowulf cluster of Raspberry Pi nodes. Int. J. Comput. Appl., 187(32), 43–55.
[8] O. Bystrov et al. (2023). Hybrid parallelization of discrete element software for heterogeneous resources. Proc. PARENG 2023.
[9] Y. Linde, A. Buzo, R. M. Gray (1980). An algorithm for vector quantizer design. IEEE Trans. Commun., 28(1), 84–95.
[10] A. H. Karp, H. P. Flatt (1990). Measuring parallel processor performance. Commun. ACM, 33(5), 539–543.
[11] Z. Wang, A. C. Bovik, H. R. Sheikh, E. P. Simoncelli (2004). Image quality assessment: from error visibility to structural similarity. IEEE Trans. Image Process., 13(4), 600–612.
Notes: Core references used in the seminar.

## Slide 40
Thank you
Questions and discussion
Ibtihal Hussien · Supervised by Dr. Ahmed Badri and Dr. Esraa Hadi · University of Babylon